## Slide 1: NCP1546/47 - Low Voltage Buck Regulator With Synchronization Capability
Market & Applications
  Consumer
Packaging & Application
  DFN – 18
Description
  4.5V to 40V Input Range
  1.5A Output
  2.0% Error Amp Reference
  Fixed Switching Frequency
    NCV1546 170kHz
    NCV1547 340kHz
  Operating Junction Temperature Range: -40~150 oC
This 1.5A buck regulator is ideal for application where the power dissipation of a linear regulator would not be sufficient.
Features
  V2TM Control Architecture
  Cycle-By-Cycle Current Limit, Short Circuit and Thermal Protection
  Sync Function
  Shutdown Mode (IQ=1uA, Typical)
  Soft Start
  Boost Pin
Benefits
  Simplified Design and Fast Transient Response
  Integrated Protection Features for Safe Operation
  Parallel Supply Operation and Noise Minimization
  Minimize Power Loss During Idle Condition
  Prevent Excessive In-rush Current and Output Over-shoot
  Maximize the IC Efficiency