## Slide 1: NCP1380 SIMPLIS MODEL GUIDE
Made by:
Stéphanie CANNENTERRE
s.cannenterre@onsemi.com

## Slide 2: About the Models
The models were built using Simplis primitive components and should be used with Simplis simulator.
They may not support Simetrix simulator.
There are two sets of schematics and NCP1380 models:
  Schematics and NCP1380 models for transient simulations:
    Schematics: “NCP1380B_Detailed_Tran_Bench.sxch” and “NCP1380B_Detailed_Tran_Bench.sxch”
    Models: “NCP1380B.sxcmp”, “NCP1380D.sxcmp”
  Schematic and NCP1380 model for AC simulation:
    Schematic: “NCP1380_AC_Simu_Bench.sxch”
    Model: “NCP1380_AC.sxcmp”

## Slide 3: Schematic for Transient Simulations
For transient simulation, use the following schematics:
  NCP1380B_Detailed_Tran_Bench.sxch
  NCP1380D_Detailed_Tran_Bench.sxch
Initial condition is set on VCC capacitor to speed the simulation time

## Slide 4: Transient Simulation Set Up
Enter your simulation analysis parameters (stop time, number of plots points)
By default, only the voltage/current at specific probes are saved. This can be changed by the user in the saves options.
Note: the transient bench schematics only support transient analysis.
  NCP1380B_Detailed_Tran_Bench.sxch
  NCP1380D_Detailed_Tran_Bench.sxch

## Slide 5: Transient Simulation Result

## Slide 6: Schematic for AC simulation
For transient simulation, use the following schematic: “NCP1380_AC_Simu_Bench.sxch”
A simplified model of NCP1380 (NCP1380_AC.sxcmp) were all the protections have been removed is used for AC simulations. This is to avoid any convergence issue.

## Slide 7: AC Simulation Set Up
Enter your simulation analysis parameters (max. period and number of cycles before launching POP)
By default, only the voltage/current at specific probes are saved. This can be changed by the user in the saves options.

## Slide 8: AC Simulation Results