## Slide 1: FAN6500X Simulation Results
11/15/2017

## Slide 2: Model Details
A simple model is provided for FAN6500X
Application circuits as below:
No Access to the inside of the FAN6500X circuit;
ILIM: A resistance connected to this pin to limit the output current;
FREQ (RT): A resistance connected to this pin to adjust the switching frequency;
FB & COMP: Two pins for appropriate Type III compensation network to control the output voltage;
SW: Output of the converter, between two FETs to be connected to inductor;
VIN: Input voltage
Note: To use the simulation model in the right way, the simulation file and FAN6500X folder should be always located in the same address as shown in the picture.

## Slide 3: Parameters for the Simulation
Vin: 35V
Vout: 28V
Cout: 75µF, ESR: 1mΩ
L: 22µH, DCR: 20.5mΩ
Compensation network for Vout, FB, and Comp:
R1: 28kΩ
R2: 613Ω
R3: 590Ω
R4: 1kΩ
C1: 2.7nF
C2: 220nF
C3: 470pF

## Slide 4: Output Results
Output current: Adjusted to 3.25A (between: 6-13 ms)
Switching Frequency: Set to 300kHz through FREQ(RT) pin