## Slide 1: NCL2801LED2GEVB Build Instructions

## Slide 2: Revision History
Revision | Date | Comment
00 | 4/11/19 | Initial Release

## Slide 3: Applicable Directives
All material and assembly processes shall comply with the directives listed here in.
RoHS 3 (EU 2015/863)
WEEE Directive (2012/19/EU)

## Slide 4: Views
Mark current revision here.

## Slide 5: Thermal Compound Placement
Add a thin layer of thermal compound between D1, D4, Q4, and their corresponding heat sinks.
Screws for each heat sink should be tightened with a torque of:
5 in/lbs ± 1 in/lbs

## Slide 6: RTV Compound
Add RTV Compound to L2, L3, and C14 as shown in the images to the right.

## Slide 7: Part Placement Notes
Ensure J1 and J6 are oriented with the contacts facing outward
All heatsinks should be placed vertically.
Ensure HS4 is aligned orthogonally with the board. The screw should be oriented with the threads facing upward and tightened with a torque of:
5 in/lbs ± 1 in/lbs

## Slide 8: Part Placement Notes
Some parts may fit backwards but SHOULD NOT be placed backwards.
The dot on top of L4 indicates pin 1 which should align with the square contact.
The light stripe on the capacitors indicates the negative pin