## Slide 1
Power Factor Correction Optimization Options
Public Information © onsemi 2022
Joel Turchi - Member of Technical Staff

## Slide 2: Agenda
Introduction
Upgraded Control Algorithms
Interleaving Channels
The Bridgeless Option
Conclusions

## Slide 3: Agenda
Introduction
Upgraded Control Algorithms
Interleaving Channels
The Bridgeless Option
Conclusions

## Slide 4: Basic PFC Definitions - Off-line Applications
The mains utility provides a sinusoidal voltage vline(t).
The shape and phase of iline(t) depend on the load.

## Slide 5:  Vline,rms  Iline,rms  cos    cos � 
Basic PFC Definitions - Generalized
cos() is the distortion factor
cos(�) is the displacement factor
The line rms current is inversely proportional to PF:
Low PF ➔ large peak and rms currents
PF  cos( )  cos(�)
Iline,rms
line,rms
Pin,avg

V
 PF
Pin,avg
iline(t)
vline(t)
iline(t)
vline(t)

## Slide 6: Some Detrimental Effects of Poor PF
High peak and rms currents
− High peak currents cause component ratings to go up
− High peak currents can cause the line to sag at sinusoid peak
− High rms currents increase dissipation in the line and circuit
− High rms currents limit available load delivery from a socket
− What power can I draw from a 16 A outlet?
PF = 1.0 | 230 . 16 . 1.0 = 3680 W | about 12 loads of 300 W
PF = 0.6 | 230 . 16 . 0.6 = 2208 W | only 7 loads of 300 W
□ Circulating currents can heat up neutral wire in 3-ɸ circuits
− Only fundamental gets cancelled, harmonics don’t
Degradation of the power quality
− Possible malfunction of other equipment on the line
− Noise and interference

## Slide 7: Power Factor Standards
EN61000-3-2: max. is specified for harmonics up to 40 (only odd ones for classes C and D)
In the 2000s, PF requirement included in other standards (e.g. Energy Star 4.0 for Computers, Climate Savers, etc.)
NO
NO
NO
NO
YES
YES
YES
YES
YES
NO
Class C
Three Phase
Equipment?
Portable Tool?
Lighting
Equipment?
Motor Equipment?
PC/Monitor or TV?
Class B
Class D
Class A
Mandatory for PC, TV sets Monitors
P > 75 W
EN61000-3-2

## Slide 8: Active Power Factor Correction (APFC)
Inserted between the line and the main converter, a pre-converter draws a sinusoidal current from the mains and provides a dc voltage
Traditionally, this is a boost converter
The driver embeds a specific control law

## Slide 9: Typical Efficiency Curves
99
98
97
96
95
94
93
92
91
90
0
20
40
80
100
120
Efficiency (%)
60
Load (%)
115 V
230 V
Efficiency curves on performance of the NCP1654 evaluation board (NCP1654PFCGEVB) reported in application note AND8324
Switching losses dominate at light load
Conduction losses dominate at full load, low line
Switching losses!
Conductio n losses!

## Slide 10: Minimizing Losses
Reducing conduction losses:
− Using low-resistance components
− Minimizing the current rms level (ripple)
− Increasing the switching frequency
Reducing the switching losses
− Using fast switches
− Implementing soft-switching techniques
− Lowering the switching frequency
!
! !

## Slide 11: Agenda
Introduction
Upgraded Control Algorithms
Interleaving Channels
The Bridgeless Option
Conclusions

## Slide 12: Operating Modes Overview
Three modes for 1-phase PFC boost converters
 | Operating Mode | Main Features
iL(t) | Continuous Conduction Mode (CCM) | Always hard-switching Inductor value is largest Minimized rms current
iL(t) | Critical conduction Mode (CrM) | Large rms current Switching frequency is not fixed
iL(t) Tclamp Tclamp | Frequency Clamped Critical conduction Mode (FCCrM) | Large rms current Frequency is limited Reduced coil inductance

## Slide 13: Critical Conduction Mode (CrM)
Most popular solution for low power applications
This scheme has several names:
− Critical Conduction Mode (“CrM”)
− Boundary Conduction Mode (“BCM”)
− BorderLine Conduction Mode (“BCM”)
− Transition Conduction Mode (“TCM”)
− Some vendors simply indicate “DCM” for Discontinuous Conduction Mode
 sin t 
 sin t 
in,rms
Vin,rms
Pin,avg

Vin,rms
Pin,avg
2 
L, pk
Vin,rms
i t   2
Pin,avg
2 
line
i (t) 
I
Current reference
L, pk
i
t 
iin t 

## Slide 14: CrM Switching Sequences
t 
iL, pk t  v (t)  t
  in on
2 2  L
T
sw
in
L
i t   i
The peak inductor current is
proportional to v (t):
in
The line current is the
averaged inductor current:
+
-
IN
Diodes Bridge
L
in
v (t)
iL(t)
+
-
IN
Diodes Bridge
in
v (t)
V
out
iL(t)
L
time
Inductor Current
vin t 
L
L
Vout  vin t 
IL, pk
in
i t 
CrM: the next current cycle starts when the core is reset
t   vin(t)  ton
L, pk L, pk
I  i
L
iL(t)
vDS(t)
Valley turn on

## Slide 15: CrM PFC - Implementation
iin t  
2
iL, pk t 
2  L
in
i (t)  vin (t)  ton
Force a sinusoid reference for iL,pk(t)
(current mode, e.g., NCL2801)
Force a constant on-time (voltage mode, e.g., NCP1611/2)
 sin t 
 sin t 
in,rms
Vin,rms
Pin,avg

Vin,rms
Pin,avg
2 
L, pk
Vin,rms
i t   2
Pin,avg
2 
line
i (t) 
I
Current reference
L, pk
i
t 
iin t 

## Slide 16: CrM – No or Low Turn-On Losses
Turning on at the valley:
  ZVS when vin(t)<Vout /2
  Turn on at vDS(t) = 2vin(t)-Vout otherwise
Tests made on NCP1612 evaluation board (NCP1612GEVB)
Inductor current reaches zero
vin (t)
vin (t)
Vout
Vout
115 V rms / 50% Load
230 V rms / 50% Load

## Slide 17: MOSFET Turn-Off in CrM
Hard-Switching Commutation
Diode tFR causes losses and an overshoot
p(t)
vDS(t)
iDS(t)
50 ns
tFR
Extracted from application note AND8123
(www.onsemi.com )

## Slide 18: CrM Large Switching Frequency Range
□ fSW varies as a function of the load and input voltage conditions
115 V rms, 160 W ➔ 91 kHz
115 V rms, 80 W ➔ 152 kHz 115 V rms, 40 W ➔ 242 kHz
Tests made on NCP1612 evaluation board (NCP1612GEVB)
4 µs
4 µs
4 µs
Vout

vin t  
fsw t  




 1
Vin,rms2
2  L  Pin,avg

## Slide 19: DCM Operation: A Good Idea?
DCM Operation:
− Lower switching losses
− Increased conduction losses

L,pk
I
CrM
ton,CrM
tdemag,CrM
tSW ,CrM
t
  SW ,DCM  1
tSW ,CrM
Ref: How2Power on-line magazine, Oct. 2012 issue (http://www.how2power.com/newsletters/1210/articles/ H2PToday1210_design_ONSemiconductor.pdf)


 CrM
Psw 
SW
P
DCM

DCM CrM
PCOND    PCOND 
IL,pk 
DCM
ton,DCM
tdemag,DCM
tSW ,DCM
dead-time
Cycle-by- cycle dead- time compensation

## Slide 20: Current Control Frequency Foldback (CCFF)
CCFF adapts the operation mode to the instantaneous value of the line current
CCFF (NCP1611/2/5)

## Slide 21: Frequency Clamped CrM Circuits
Frequency Foldback optimizes the light-load efficiency
Obtained with the NCP1612 160-W, wide-mains EVB. See http://www.onsemi.com/pub/Collateral/EVBUM2051-D.PDF for more details

## Slide 22
0
Efficiency (%)
10 20 30 40 50 60 70 80 90 100
Load (%)
Conduction losses dominate
Switching losses dominate
L
FCCrM Optimizes The Inductor Size
FCCrM: no need for “over-dimensioning” L for light load
For similar performance:
CrM requires
FCCrM requires
300 µH for a 150-W application
150 µH for a 150-W application (e.g., NCP1631 evaluation board)
max
L  45 mH  W / Pin,avg 
L  30 mH  W / Pin,avg 
max
or FC
Increasing L

## Slide 23: CrM – Too Large A Current Ripple For High Power
Large ripple of the inductor current
Bulk capacitor high rms current
Need for differential-mode EMI filtering
Large conduction losses
CCM preferred above 300 W
iin(t)
2.iin(t)
iL(t)
-ILOAD
2.iin(t)
iC(t)

## Slide 24: CCM PFC - Inductor Current
No ZCS ➔ Need for a low trr diode
The ratio iL(t) over iin(t) is small
The current ripple depends on L and vin(t):
“Instantaneous”:
in
At v (t) top:






pk  pk
out
sw
L
I 
V
L  f
 in,rms 1 in,rms 
2 V 2 V

sw  out 
vin t   vin t 
IL pk  pk t   1
L  f V

## Slide 25: CCM vs CrM
□ 33% lower MOSFET and inductor conduction losses
Dc current most critical for the boost diode
 | CCM | CrM
IL,rms | Pin,avg Vin,rms |  Pin,avg Vin,rms
IQ,rms | Pin,avg  1 8 2 Vin,rms Vin,rms 3 Vout | 2  Pin,avg  1 8 2 Vin,rms 3 Vin,rms 3 Vout
ID,rms | Pin,avg  8 2  Vin,rms Vin,rms 3 Vout | 2  Pin,avg  8 2  Vin,rms 3 Vin,rms 3 Vout

## Slide 26: CCM Turn On Losses
Diode losses during the switching event:
MOSFET turn on losses:
Significant losses
Peter Haaf and Jon Harper, “Understanding Diode Reverse Recovery and its Effect on Switching Losses”, Fairchild Power Seminar 2007, https://www.fairchildsemi.com/technical- articles/Understanding-Diode-Reverse-Recovery-and-Its-Effect-on-Switching-Losses.pdf
VKA
V
DS
I
DS
I
D
time
time
time
time
L
I
L
I
VOUT
VOUT
IRRM
IRRM
B
t
A
t
tRR
t1
 V  I  t V  I  t V  I  t

p 
 f
D 
 SW


2
2
F L 1  F RRM A  OUT RRM B
6
RRM
Q,on OUT
SW

p  V  

  f

L 1 A B
 I  t  2  t  t  I  3  t  2  t  
2
A B
6

## Slide 27: CCM, CrM and DCM Operation Modes
□ The cycle duration of the inductor current sets the operation mode
FCCrM: Frequency Clamped Critical Conduction Mode
Tclamp
Vclamp
Internal Ramp
VDS
iL(t)
Tclamp
Vclamp
Internal Ramp
VDS
TCCM
Vramp,pk
Internal Ramp
VDS
iL(t) iL(t)
Tcycle < Tclamp ➔ DCM Tclamp < Tcycle < TCCM
Automatic selection of the mode
CrM
Tcycle > TCCM
CCM

## Slide 28: Why Multimode PFC?
Best conduction mode in all line/load conditions
  DCM for light load
  CrM for medium load
  CCM for heavy load
The NCP1618 firmly controls the switching frequency:
65 kHz (with jittering) when in heavy load conditions (CCM)
58 kHz to 130 kHz in critical conduction
130 kHz to 25 kHz in DCM (with frequency foldback)
High efficiency over the load range
Eased EMI filtering
500-W EVB efficiency @ 115 V

## Slide 29: Wide-mains, 500-W EVB
Description | Value | Units
Input Voltage Range | 90-265 | V rms
Line Frequency Range | 45 to 66 | Hz
Output Power | 500 | W
Nominal Output Voltage | 390 | V
Minimum Output Load Current | 13 | mA
Maximum Output Load Current | 1300 | mA
Load Conditions For Efficiency Measurements (10%, 20%,..) | 10-100 | %
Minimum Efficiency Over Above Load Range, 115 V rms | 94 | %
Minimum PF Over The Line Range At Full Load | 95 | %
Hold-Up Time (the output voltage remaining above 300 V) | > 10 | ms
Peak-To-Peak Low Frequency Output Ripple | < 8 | %
More details at: https://www.onsemi.com/pub/Collateral/EVBUM2716- D.PDF

## Slide 30: Line Current @ 115 V rms
CCM
CrM
Frequency Clamped CrM
Frequency Foldback

## Slide 31: Operation modes at 115 V rms, 40% load
a) Top of the sinusoid b) Near the line zero crossing
Critical conduction mode at the sine-wave top
The 130-kHz frequency clamp forces DCM near the line zero crossing
Valley turn on in both cases
I
LINE
Vout
VDS
ILINE
Vout
VDS
10 µs
10 µs

## Slide 32: Operation modes at 115 V rms, 20% load
a) Top of the sinusoid b) Near the line zero crossing
Frequency foldback leads to low frequency operation (about 30 kHz)
The number of valleys adapts to the VDS resonant period without repeated, unnecessary changes in the number of valleys (stable and silent operation)
Valley turn on in both cases
Efficient light-load operation
ILINE
Vout
VDS
ILINE
Vout
VDS
20 µs
40 µs

## Slide 33: Efficiency over the load range
The efficiency is measured after a 30-mn warm-up time at full load. The load is decreased from 1.30 A down to 0.13 A by 0.13-A steps. The measure is made after 5 mn at the operating point under test.
The efficiency remains above 94% from 10% to 100% of the load at the 4 tested line levels (90 V rms, 115 V rms, 230 V rms and 265 V rms).

## Slide 34: PF and THD Performance
On the 20% to 100% load range, the power factor remains higher than 0.9 and the THD well below 20% at the four tested line levels.

## Slide 35: Agenda
Introduction
Upgraded Control Algorithms
Interleaving Channels
The Bridgeless Option
Conclusions

## Slide 36: Interleaved PFC - Main Characteristics
Two small PFC stages in lieu of a single big one
If the two channels are out-of-phase, the resulting currents (IL(tot)) and (ID(tot)) exhibit a dramatically reduced ripple.
NCP1631
EMI
Filter
LOAD
7
10
Branch 1
Branch 2
L(tot )
I
ID(tot )
L1
I
D1
I
IL2
ID2
Vin
Vout
Cbulk
in
in
C
cc
V
Rsense
Vaux1
aux2
V
I |  |  | 1 2 | 31 | 16 15
 |  |  | 3 | 16 | 14
 |  |  | 4 | P | 13
 |  |  | 5 |  | 12
 |  |  | 6 | NC | 11
 |  |  | 8 |  | 9
Ac line

## Slide 37: Interleaved PFC - Benefits
More components but:
− A 250-W PFC is easier to design than a 500-W one
− Modular approach
− Better heat distribution – easier cooling
− Smaller (more standard) components
− Two CrM PFCs look like a CCM PFC converter…
  Interleaving allows for a reduced input current ripple
eased EMI filtering
Reduced output rms current
Lower stress on the bulk capacitor
Current ripple of each phase cancels!
time
IL(tot)
IL2
IL1

## Slide 38: Interleaved PFC - Input Current Magnitudes
 | v (t)  Vout in 2 | v (t) � Vout in 2
Averaged input | iin (t)  iL(tot ) t   Tsw | vin t   vin t   Pin,avg Rin Vin,rms2
current |  | 
(line current) |  | 
Peak to peak ripple | I   i t   1 vin t   L(tot ) pk  pk in  V  v t    out in  | I   i t    2  Vout  L(tot ) pk  pk in  v t    in 
Peak Current | I   2  i t   1 Vout  Ltot  in   pk  4  Vout  vin t     | I   2  i t   1 Vout  Ltot  pk in  4  v t    in 
envelope |  | 
Valley Current | I   i t   Vout Ltot  v in 2  V  v t  out in | I     Pin,avg Vout L tot v 2 Vin,rms2
envelope |  | 
Current pk-pk ripple is independent from L
It is nearly iin(t) /2 @ 90 V rms (top of the sinusoid)
See https://www.onsemi.com/pub/Collateral/AND8355-D.PDF

## Slide 39: Interleaved PFC - Boost Diode Current
The boost diode(s) current depends on the mode:
Phase 1
Phase 2
Single phase CCM
Single phase CrM
Interleaved CrM
3
in
vin t 
Vout
2  i t  
in
vin t 
Vout
t  
1  2  i
2 3
rms value over Tsw
rms value over Tsw
rms value over Tsw
in
vin t 
Vout
i t  
2  iin t 
iin t 
iin t 
iin t 

## Slide 40: Interleaved PFC - Capacitor Rms Current
Integration over the sinusoid leads to (resistive load):
 | Single-phase CCM PFC |  | Single-phase CrM / FCCrM* PFC |  |  | Interleaved CrM / FCCrM* PFC |  | 
Diode(s) |  |  P 2 8 2   out     3 Vin,rms Vout |  |  |  |  |  | 
rms current | I1  |  | 2  I1 3 |  |  | 2  I1 3 |  | 
(ID,rms) |  |  |  |  |  |  |  | 
CBULK rms current | I 2  I 2 1 out |  | 4  I 2 1 3 |  Iout  | 2 | 2  I 2 1 3 |  Iout  | 2
(IC,rms) |  |  |  |  |  |  |  | 
300-W, Vout = 390 V Vin,rms = 90 V | ID,rms = 1.9 A IC,rms = 1.7 A |  | ID,rms = 2.2 A IC,rms = 2.1 A |  |  | ID,rms(tot) = 1.5 A IC,rms = 1.3 A |  | 
Interleaving dramatically reduces the rms currents
  reduced losses, lower heating, increased reliability
* Frequency Clamped CrM

## Slide 41: Interleaved reduces the conduction losses
□ MOSFET and Inductance conduction losses are divided by the number of channels
 | One-phase CrM | CCM | Interleaved CrM
IL,rms | 2  Pin,avg 3 Vin,rms | Pin,avg Vin,rms | 1  Pin,avg 3 Vin,rms
IQ,rms | 2  Pin,avg  1 8 2 Vin,rms 3 Vin,rms 3 Vout | Pin,avg  1 8 2 Vin,rms Vin,rms 3 Vout | 1  Pin,avg  1 8 2 Vin,rms 3 Vin,rms 3 Vout
ID,rms | 2  Pin,avg  8 2  Vin,rms 3 Vin,rms 3 Vout | Pin,avg  8 2  Vin,rms Vin,rms 3 Vout | 1  Pin,avg  8 2  Vin,rms 3 Vin,rms 3 Vout
 | One-phase CrM | CCM | Interleaved CrM
 pCOND  L | 2 4  r   Pin,avg  3 L  V   in,rms  |  P 2 r   in,avg  L  V  in,rms | 2 2  r   Pin,avg  3 L  V   in,rms 
IQ,rms | 2 4  R   Pin,avg   1 8 2 Vin,rms  3 DS on  V   3 V   in,rms   out  |  P 2  8 2 V  R   in,avg   1 in,rms  DS on  V   3 V   in,rms   out  | 2 2  R   Pin,avg   1 8 2 Vin,rms  3 DS on  V   3 V   in,rms   out 

## Slide 42: Interleaved Benefits (CrM or CCM)
□ Like if the MOSFET and inductors were simply paralleled, conduction losses are divided by the number of phase
In addition, the current ripple is dramatically reduced
− Less EMI filtering required, eased use of low-resistance components
− Lower magnetic losses
Comparable switching losses compared to single-phase PFC operating in same mode

## Slide 43: Agenda
Introduction
Upgraded Control Algorithms
Interleaving Channels
The Bridgeless Option
Conclusions

## Slide 44: Bridgeless PFC - Introduction
The diodes bridge rectifies the ac line voltage
Two diodes conduct simultaneously
Two diodes in the current path
Ac line
EMI
filter
PFC
stage
+
D1
+
240 AIO EVB
NCP1631 PFC EVB
D4
D3
D2

## Slide 45: Input Bridge Losses
Average current flowing through the input diodes:
Dissipation in the diodes bridge:
If Vf = 0.85 V and (Vin,rms)LL = 90 V:
  In low mains applications (@ 90 V rms),
the diodes bridge wastes about 1.7% efficiency!
bridge
P

� 1.7%  Pout
line
Tline
bridge Tline
I

 I (t) 
2 2 
Pout
 Vin,rms
bridge
f bridge
f
P
 2 V  I
 2 V
 2 2  Pout
  Vin,rms

## Slide 46: Bridgeless Benefit
Nearly constant benefit over the load range
Reduced gain in light load due to lower VF
Mainly line-dependent benefit
0
Efficiency (%)
10 20 30 40 50 60 70 80 90 100
Load (%)
90 V rms
265 V rms
0
Efficiency (%)
10 20 30 40 50 60 70 80 90 100
Load (%)
Bridgele ss
Convention
al
Bridgele ss
Convention al
1.7%
0.6%

## Slide 47: Two-Boost Bridgeless PFC
Two PFC stages but:
− One driver with no need for detecting the active half-wave
− Improved thermal performance
− As with conventional PFC stages, the negative phase is always attached to ground.
EMI issue is solved.
« PH1 » PFC
stage
« PH2 » PFC
stage
Ac Line
PH1
PH2
DRV
Reference: Alexandre Ferrari de Souza and Ivo Barbi, “High Power Factor Rectifier with Reduced Conduction and Commutation Losses”, Intelec, 1999
D1
D2

## Slide 48: Equivalent Schematics for the Half-Line Cycles
Ac Line
PH1
PH2
DRV
+
-
D1
PH2 PFC stage
Ac Line
PH2
DRV
+ PH1
-
D
2
PH1 PFC stage
Terminal PH1 is the high one
Terminal PH2 is the high one
Only one diode on the current path

## Slide 49: Two-Boost Bridgeless vs Interleaving - Boards
PQ32/20 (115 µH / 10 A pk) PQ26/20 (150 µH / 5 A pk)
220 µF / 450 V
100 µF / 450 V
Controllers:
NCP1605 for Bridgeless PFC (clamp frequency set to 130 kHz)
NCP1631 for interleaved PFC (clamp frequency set to 130 kHz per branch)
Current Sense Transformers

## Slide 50: Two-Boost Bridgeless vs Interleaving - Efficiency @ 90 V
Light-Load Management Functions being disabled in both circuits (soft-skip mode for NCP1605 and Frequency Foldback for NCP1631)
Efficiency (%)
97.0
96.5
96.0
95.5
95.0
94.5
94.0
93.5
93.0
92.5
92.0
0 10 20 30 40 50 60 70 80 90 100 110
Load (%)
Efficiency (%)
97.0
96.5
96.0
95.5
95.0
94.5
94.0
93.5
93.0
RDS(on) = 99 m @ 25°C
92.5
92.0
0 10 20 30 40 50 60 70 80 90 100 110
Load (%)
RDS(on) = 250 m @ 25°C
92.5
92.0
94.0
93.5
93.0
97.0
96.5
96.0
95.5
95.0
94.5
0
10
20
30
40
70
80
90
100
110
Efficiency (%)
50 60
Load (%)
Solid lines: rDS(on) = 99 m @ 25°C Dashed lines: rDS(on) = 250 m @ 25°C
Blue: Bridgeless Red: Interleaved

## Slide 51: Two-Boost Bridgeless vs Interleaving – High Line Data
At high-line, the bridgeless advantage reduces.
Low rDS(on) does not improve. MOSFET parasitic capacitance degrades the performance particularly for interleaving
(2 times more switching events)
94.5
96.0
95.5
95.0
97.5
97.0
96.5
98.0
98.5
99.0
0
10
20
30
40
70
80
90
100 110
Efficiency (%)
50 60
Load (%)
97.0
96.5
96.0
98.0
97.5
99.0
98.5
Efficiency (%)
95.5
95.0 rDS (on )  99 m @ 25 C
94.5
0 10 20 30 40 50 60 70 80 90 100 110
Load (%)
rDS (on )  250 m @ 25 C
Interleaved
Interleaved
Bridgeless
Bridgeless
0.2 %
0.4 %

## Slide 52: True Bridgeless - Rearranging classical boost converter
AC
L O A D
Move the inductor in series with ac line
Low-Frequency Leg
High-Frequency Leg. WBG switches needed for CCM,
SJ FETs w. low QRR viable for CrM.

## Slide 53: Totem Pole PFC
Totem Pole is an elegant 4-switch boost solution that reduces number of components in the current path.
1 FET in the “diode” section (Low-Freq leg) and 1 FET in the boost section conducting.
AC
L
O A D
Slow Leg Line Frequency
Fast Leg PWM Frequency
SRH
SRL
PWMH
PWML

## Slide 54: Positive Half Cycle Operation
S2 is the duty cycle (d) controlled device and S1 is the (1-d) device
When S2 is on, VL = VAC and current (blue path) circulates through S2 and SR2
When S2 turns off, VL = VAC - VO and current free wheels through S1 and SR2 (red path). S1 can be turned on for increased efficiency
SR2 is returning current to the source for the entire positive line cycle

## Slide 55: Negative Half Cycle Operation
S1 is the duty cycle (d) controlled device and S2 is the (1-d) device
When S1 is on, VL = - VAC and current (blue path) circulates through S1 and SR1
When S1 turns off, VL = VAC - VO and current free wheels through S1 and SR2 (red path). S2 can be turned on for increased efficiency
SR1 is returning current to the source for the entire negative line cycle

## Slide 56: 300-W NCP1680 Evaluation Board
A high efficiency over the entire load/line range !
97%

## Slide 57: 500-W NCP1681 Evaluation Board
96%
A high efficiency over the entire load/line range !

## Slide 58: Totem Pole vs. Standard Boost - Efficiency Comparison on a 500 W PFC
93,00
92,00
94,00
95,00
97,00
96,00
98,00
100,00
99,00
0
10
20
30
40
50
Load (%)
60
70
80
90
100
Efficiency (%)
Totem Pole vs. Standard Boost Efficiency @ 90 Vac
Totem Pole Eff
Std. Boost Eff
1.8% efficiency gain 30% reduction in losses
~ 9 W savings
500 W
Totem Pole utilizes 2 eGaNs & 2 SJ FETs
Standard boost uses 2 SJ FETs & 1 SiC diode

## Slide 59: Agenda
Introduction
Upgraded Control Algorithms
Interleaving Channels
The Bridgeless Option
Conclusions

## Slide 60: Conclusions – Take-Aways
CrM is a popular and efficient solution for low power
Frequency clamp helps optimize the inductor size and cost
Frequency reduction techniques necessary for light-load efficiency
CCM is the most practical solution for high-power operation
Multimode PFCs automatically select the best conduction mode
Multimode PFCs provide optimized performance over the line/load range
Interleaving requires more components but dramatically reducing the current ripple
Interleaving increases the CrM power range
Bridgeless further improves the low-line efficiency over the entire load range
Totem Pole PFC provides superior performance

## Slide 61
Follow Us @onsemi
www.onsemi.com