## Slide 1: USING LINEAR SUPERPOSITION TO SOLVE MULTIPLE HEAT SOURCE TRANSIENT THERMAL PROBLEMS
Roger Stout, P.E.
Senior Research Scientist
roger.stout@onsemi.com
David Billings, P.E.
Associate Research Scientist
david.billings@onsemi.com
(Presenter)
InterPACK '07

## Slide 2: Outline
Setting up the Problem- Data collection
Curve Fitting a R-Tau Model to Transient Data
Using Linear superposition to solve Complex waveforms in Excel™
Using Linear superposition to solve Complex waveforms in Electrical Spice
Conclusion/ Recommendations
References
Notes: The purpose behind this seminar is twofold:
To show how to analyze a multiple-heat-source transient thermal system by applying the principles of linear superposition; and how to solve these problems using tool available to most Electrical or Product engineers.
We’ll cover the relevant topics in a systematic way, as indicated in this outline.

## Slide 3: Setting up the Problem- Data collection
Each heat source needs to be independently heated.
Each potential measurement location needs to be monitored.
  Measurement techniques require high speed data acquisition for multiple inputs. A method of converting voltage from a device to a temperature from a calibrated source.
  Simulation techniques require tracking temperature locations and storing the values for later processing.
Transient temperature data must then be converted to a transient impedance curve and fit to a R-Tau net-list.

## Slide 4: Each heat source needs to be independently heated.
Each heat source needs to be independently measured based on the interaction of the others.
Power input (W)
Time (sec)
Time (sec)
Temperature (°C)
Thermal System Boundary
Measurement cycle(s)

## Slide 5: Converting Temperature data into Thermal resistance values for R-Tau model fit.
Temperature correction for the first millisecond can be performed for a surface flux heat source input using the square-root of time estimate.
(MIL-STD 883 method 1012, Heat Transfer, J.P Holman 5th edition)
[units °C-mm^2-√sec/W]
[units °C/W]
Definitions:
A area of the surface being heated
L thickness of the material
ρ density of the material
Cp Specific heat of the material
K thermal conductivity of the material
Csr square-root-of-time constant
Csr_eff parallel combination of Csr constants
R(t) thermal response as a function of time
sqrt(t) square-root-of time abbreviation
C thermal capacitance
t time
Tau thermal time constant

## Slide 6: Converting Temperature data into Thermal resistance values for R-Tau model fit. (Continued)
Measured data typically is very noisy because of the switching from a heating condition to a measurement state. This can last up to 1 millisecond or longer depending on the device characteristics.
  We heat to steady state then switch to measurement and watch the complete cooling curve to eliminate as much noise as possible. It limits our power input to a steady state value but enhances our measurement accuracy and noise reduction.
Switching noise
Square-root of time correction

## Slide 7: Converting Temperature data into Thermal resistance values for R-Tau model fit. (Continued)
Simulated data typically is affected by the short time response of the elements. Elements that are too thick relative to the heat flow direction will under predict the temperature rise.
There is a trade off between model solution time and size and temperature response. As long as we understand where this limitation begins we can correct for the discrepancies using the square-root of time estimate
Thick element response
Square-root of time correction

## Slide 8: Converting Temperature data into Thermal resistance values for R-Tau model fit. (Continued)
Understanding that the square-root of time estimates for a surface flux heat source improves the model, we can take it one step further to improve the curve fitting for a lumped parameter network.
Lumped parameter models suffer the same problems of finite element models. A lump too large will respond too slowly to represent the actual system.
Breaking the short time response lumps into smaller and faster responding lumps improves the accuracy of the model.
This allows us to resize the model for quicker response if need be.
A Method of spliting the short time response:
R1=Csr_eff*SQRT(Tau1)
R2=Csr_eff* SQRT (Tau2)-R1
R3=Csr_eff* SQRT (Tau3)-R1-R2
R4=Csr_eff* SQRT (Tau4)-R1-R2-R3
4 resistor split with decreasing R & Tau values
Single Lump representing the short time response

## Slide 9: Converting Temperature data into Thermal resistance values for R-Tau model fit. (Continued)
A Foster network can be easily represented in Excel as an array formula with a combination of a few key strokes. [Control+Shift+Enter] which add the braces {} to the formula.
Adding a fit error function to show the difference between input data and fit data helps to visualize model fit overall.
H
E
A
T
R1
R2
C1
C3
R3
C2
Cn
Rn
Taui = Ri * Ci
{=SUM(R1:R10*(1-EXP(-t/Tau1:Tau10)))}
Fit Error= delta between model and fit
@ a particular time value
Fit error function=SQRT(SUMSQ(delta1:delta2))
Used to optimize the overall curve fit

## Slide 10: Converting Temperature data into Thermal resistance values for R-Tau model fit. (Continued)
Using the “solver” feature in Excel can also be used to minimize the error between input data and R-C model.
After optimization

## Slide 11: Final R-Tau model fit.
Although a little manual manipulation may be required to ensure convergence as well as constraining the end points of the model.
 | R's | Tau's
1 | 0.13096 | 1.00E-06
2 | 0.28318 | 1.00E-05
3 | 0.89549 | 1.00E-04
4 | 1.47 | 0.0008
5 | 4.93 | 0.036
6 | 40.94 | 0.269
7 | 33.27 | 1.348
8 | 43.49 | 6.705
9 | 0.010 | 20.604
10 | 229.3 | 67.244
Csr_eff=130.9
R1=Csr_eff*SQRT(Tau1)
R2=Csr_eff* SQRT (Tau2)-R1
R3=Csr_eff* SQRT (Tau3)-R1-R2
R10=Max R(t) from data – SUM(R1:R10)
Highlighted values are allowed to be changed by the solver. The other values are fixed by definition.
This is then repeated for every temperature heat source.
Non heated elements do not require the sqrt(t) correction as the first three rows show in this example.
{=SUM(R1:R10*(1-EXP(-t/Tau1:Tau10)))}
Subject to these Constraints
R4:R9>0.01
Tau4:Tau10>1e-6

## Slide 12: Assembling into blocks for Superposition solution
R-Tau FOSTER NET-LIST BLOCK FOR D1 ONLY
Each block is assembled for each heat source self heating network and the networks interactions with the other heat sources.
Thermal equivalent Resistor – Capacitor networks
Self Heating Network (R-Tau)
Thermal equivalent Resistor – Capacitor networks
Interaction Heating Networks (R-Tau)

## Slide 13: Organizing the sheet for transient solution
A section for power input to the heat sources
A section for power changes
A section for Temperature response calculation
A cell for keeping track of the overall time progression of ALL blocks.
A section for Time changes
=IF(Master_Time>Row_Time,Master_time-Row_time,0)
Self heating column (each cell is a separate array formula)
{=dP-D#*SUM(R1:R10*(1-EXP(-dtime/Tau1:Tau10)))}
Interaction heated columns (each cell is a separate array formula)
{=dP-D#*SUM(R5:R10*(1-EXP(-dtime/Tau5:Tau10)))}

## Slide 14: Table for plotting temperature output
=SUM(D1:D1_by_D4) +T_ambient
Note!
Time in this column can be independent of the time values in the power input section
Next, Select this whole region
Apply a
Data > Table option

## Slide 15: Final plotted Results
0
0.5
1
1.5
2
2.5
3
0
0.05
0.1
0.15
0.2
0.25
0.3
Time (Sec)
Temperature (C)
0
0.5
1
1.5
2
2.5
3
0
0.05
0.1
0.15
0.2
0.25
0.3
Time (Sec)
Temperature (C)
0
0.2
0.4
0.6
0.8
1
1.2
1.4
0
0.05
0.1
0.15
0.2
0.25
Time (Sec)
Power (W)
D1
0
0.2
0.4
0.6
0.8
1
1.2
1.4
0
0.05
0.1
0.15
0.2
0.25
Time (Sec)
Power (W)
0
0.2
0.4
0.6
0.8
1
1.2
1.4
0
0.05
0.1
0.15
0.2
0.25
Time (Sec)
Power (W)
0
0.2
0.4
0.6
0.8
1
1.2
1.4
0
0.05
0.1
0.15
0.2
0.25
Time (Sec)
Power (W)
0
0.5
1
1.5
2
2.5
3
0
0.05
0.1
0.15
0.2
0.25
0.3
Time (Sec)
Temperature (C)
T_D1
T_D2
T_D3
T_D4
0
0.5
1
1.5
2
2.5
3
0
0.05
0.1
0.15
0.2
0.25
0.3
Time (Sec)
Temperature (C)
Last power input
D2
D3
D4

## Slide 16: Spice Thermal Simulation
Using an electrical analogy to do thermal analysis the following rules apply:
Electrical | Thermal
Voltage (V) | Temperature difference (°C)
Current (A) | Power (W)
Resistance (Ω) | Thermal resistance (°C/W)
Capacitance (farad) | Thermal capacitance (W-sec/°C) [Tau/R]

## Slide 17: Components of a Spice model
Piece–wise linear current source for Power input from each source generating heat.
Summing tool to add voltages from the separate interaction networks with the self heating network
Thermal ground – by adding a voltage potential to the ground point ambient temperature can be added.
Thermal equivalent Resistor – Capacitor networks
The Output port (OUT1) will be where you want to monitor the temperature response
Each heat source will require a similar block in order to simulate the temperature response of the self heating effect as well as the interactions.

## Slide 18: Conclusions
With the right tools a Thermal R-C network can be generated from temperature data which is captured from measurements or Finite Element simulation.
The method allows for generating complex – compact transient thermal models with several heat sources.
Many problems can be solved using a spread sheet tool like Excel™ from Microsoft®.
The method can also be performed using Electrical tools such as SPICE or P-SPICE. (Assuming a voltage summing tools is available in the library.)

## Slide 19: Recommendations
Temperature dependences of power can be added but may cause solution instability in tools such as Excel.
Model size can get to the point of overwhelming the computational capability of the computer.(>100 networks)
Foster Networks can be used to simulate the thermal response of a system using commonly available software tools, where as Cauer networks (which are closer to a physical lumped system) are not.
Cauer Networks are also harder to generate physically representative lumped parameters models.

## Slide 20: References
1- D. E. Mix and A. Bar-Cohen, “Transient and Steady
State Thermo-Structural Modeling of a PDIP
Package”, Proceedings of the ASME Winter Annual
Meeting, Nov. 1992, ASME
2- “Accuracy and Time Resolution in Thermal Transient
Finite Element Analysis,” ANSYS 2002 Conference &
Exhibition, April 2002, R.P. Stout & D.T. Billings
3- “A Conjugate Numerical-RC Network Prediction of
the Transient Thermal Response of a Power Amplifier
Module in Handheld Telecommunication,” InterPACK
2005, July 2005, T.Y. Lee, V.A. Chiriac, R.P. Stout
4- AND8223-D Predicting Thermal Runaway. Roger
Stout, Available at www.onsemi.com.
5- W.J. Hepp, C.F.Wheatley, “A New PSICE Subcircuit
For the Power MOSFET Featuring Global
Temperature Options’, IEEE Transactions on Power
Electronics Specialist Conference Records, 1991 pp.
533-544
6- F Di Giocanni, G. Bazzabi, A. Grimaldi, “A New
PSPICE Power MOSFET Subcircuit with Assoicated
Thermal Model”, PCIM 2002 Europe, pp. 271-276
7- M.Marz, P.Nance, “Thermal Modeling of Powerelectronics Systems”, Infineon Technologies,
Application Note, mmpn_eng.pdf.
8- A Laprade, S.Pearson, S. Benczkowsi, G. Dolny, F.
Wheatley “ A Revised MOSFET Model with Dynamic
Temperature Compensation” Fairchild Semiconductor
Application note 7533, Oct 2003.
9- “Model Transient Voltage Suppressor Diodes” Steve
Hageman, MicroSim Application Notes, Version 8.0
June 1997, pp. 134-146
10- AND8214-D General Thermal RC Networks. Roger
Stout, Available at www.onsemi.com
11- AND8218-D How to Extend a Thermal-RC-Network
Model,. Roger Stout, www.onsemi.com
12- AND8219-D Duty Cycle and Thermal Transient
Response, Roger Stout, www.onsemi.com
13- AND8221-D Thermal RC Ladder Networks, Roger
Stout, www.onsemi.com